MEEn 537
HW 4
Jae Lee

As far as I observed, there was no specific positions that the robot couldn’t get to as long as the desired position is within the workspace of the robot. Depending on starting configuration or method used, it takes longer or shorter time to get to the desired point.

Results
For the desired_position = [-0.5441, -0.2738, 0.7873] / q1 = [0 0 0 0 0 0] / q2 = [pi/2 pi/2 pi/2 pi/2 pi/2 pi/2] / The following is the result for the method 2, 3 and different starting positions(q1, q2). / ==========Method 2, q1========== / num_iteration = 114 / final_joint_angles = [-0.2708 -1.1808 -1.2011 -0.1502 -0.9268 0] / ==========Method 2, q2========== / num_iteration = 282 / final_joint_angles = [0.7674 2.6279 1.9709 1.0606 0.9027 1.5708] / ==========Method 3, q1========== / num_iteration = 52 / final_joint_angles = [-0.0580 -1.2936 -1.1925 -0.0950 -0.5824 0] / ==========Method 3, q2========== / num_iteration = 244 / final_joint_angles = [0.7610 2.6184 1.9766 1.0679 0.8942 1.5708] / ==========Original q1========== / ==========Original q2==========

Code
%MDL_HW_2 / clear; close all; clc; / clear L / %%%%%%%%%%%%% theta, d, a, alpha, revolute or prismatic, offset / L(1) = Link([ 0 0.2 0 -pi/2 0 0], 'standard'); / L(2) = Link([ 0 0. 0.2 0 0 0], 'standard'); / L(3) = Link([ 0 0. 0 pi/2 0 pi/2], 'standard'); / L(4) = Link([ 0 0.4 0 -pi/2 0 pi/2], 'standard'); / L(5) = Link([ 0 0.0 0 pi/2 0 0 ], 'standard'); / L(6) = Link([ 0 0.4 0 0 0 0], 'standard'); / %% defining the robot now / robot = SerialLink(L, 'name', 'HW 4', ... / 'manufacturer', 'Killpack Inc.'); / % some useful poses / q1 = [0 0 0 0 0 0]; % zero angles, L shaped pose / q2 = [pi/2 pi/2 pi/2 pi/2 pi/2 pi/2]; / num_tests = 1; / %generating random joint angles with joint limits / jt_angles = random('uniform', -pi/2, pi/2, 6, num_tests); / %making emtpy vector to store positions / positions = zeros(3, num_tests); / %calculating FK for each set of random joint angles / for i=1:num_tests / FK = robot.fkine(jt_angles(:,i)); / positions(:, i) = FK(1:3, 4); / end / %%========== method 2 ========== / % starting configuration with q1 / k = 1; / gain = 1; / kappa = [gain*eye(3); zeros(3)]; / threshold = 0.1; / time_step = 0.1; / for i=1:num_tests / q = q1; / error = 100; / iteration = 0; / while error > threshold / J = robot.jacob0(q); / J_A = [eye(3) zeros(3); zeros(3) zeros(3)]*J; / current_fk = robot.fkine(q); / current_position = current_fk(1:3,4); / q_dot = J_A'*inv(J_A*J_A' + k^2*eye(6))*(kappa*(positions(:,i)-current_position)); / q = q + q_dot'*time_step; / robot.plot(q); / iteration = iteration+1; / error = norm(current_position-positions(:,i)) / end / disp('==========Method 2, q1=========='); / desired_position = positions(:,i) / num_iteration = iteration / final_joint_angles = q / end / % starting configuration with q2 / for i=1:num_tests / q = q2; / error = 100; / iteration = 0; / while error > threshold / J = robot.jacob0(q); / J_A = [eye(3) zeros(3); zeros(3) zeros(3)]*J; / current_fk = robot.fkine(q); / current_position = current_fk(1:3,4); / q_dot = J_A'*inv(J_A*J_A' + k^2*eye(6))*(kappa*(positions(:,i)-current_position)); / q = q + q_dot'*time_step; / robot.plot(q); / iteration = iteration+1; / error = norm(current_position-positions(:,i)) / end / disp('==========Method 2, q2=========='); / desired_position = positions(:,i) / num_iteration = iteration / final_joint_angles = q / end / %%========== method 3 ========== / % starting configuration with q1 / gain = 1; / kappa = [gain*eye(3); zeros(3)]; / threshold = 0.1; / time_step = 0.1; / for i=1:num_tests / q = q1; / error = 100; / iteration = 0; / while error > threshold / J = robot.jacob0(q); / J_A = [eye(3) zeros(3); zeros(3) zeros(3)]*J; / current_fk = robot.fkine(q); / current_position = current_fk(1:3,4); / q_dot = J_A'*(kappa*(positions(:,i)-current_position)); / q = q + q_dot'*time_step; / robot.plot(q); / iteration = iteration+1; / error = norm(current_position-positions(:,i)) / end / disp('==========Method 3, q1=========='); / desired_position = positions(:,i) / num_iteration = iteration / final_joint_angles = q / end / % starting configuration with q2 / for i=1:num_tests / q = q2; / error = 100; / iteration = 0; / while error > threshold / J = robot.jacob0(q); / J_A = [eye(3) zeros(3); zeros(3) zeros(3)]*J; / current_fk = robot.fkine(q); / current_position = current_fk(1:3,4); / q_dot = J_A'*(kappa*(positions(:,i)-current_position)); / q = q + q_dot'*time_step; / robot.plot(q); / iteration = iteration+1; / error = norm(current_position-positions(:,i)) / end / disp('==========Method 3, q2=========='); / desired_position = positions(:,i) / num_iteration = iteration / final_joint_angles = q / end